## Slide 1: Optickle 2

## Slide 2: New Features
Multiple wavelength support
  optics can have different properties (e.g., reflectivity) for different wavelengths
Polarization support
  similar to wavelength, optics can specify polarization dependent properties
Non-linear optics support
  squeezer implemented

## Slide 3: New Features (2)
TEM10 support (yaw)
  quantum noise for 01 and 10
Output matrix implemented
  quantum noise computed after output matrix
  enables homodyne detection

## Slide 4: Bug Fixes
Radiation pressure now works properly for transmissive optics with high power incident on both sides
Guoy phases and complex Q basis values now follow standard convention (were conjugates)
TEM01/10 modes calculations now include half-plane integration coefficient sqrt(2/pi)

## Slide 5: Backward Compatibility
Optickle1 models should work
However, for TEM01/10 models…
  because of convention changes, some external codes may break
  you will need to check gains and signs
Use of Matlab’s current OOP capability means that a lot of old code can be simplified, or at least new code should not follow the old examples

## Slide 6: To Do List
Input matrix
  no new capability, but convenient
tickle2, with no “mevans-meters”
  mevans-meters - “the displacement you would get if there we no opto-mechanics”
  separate optical TFs from opto-mechanics, the product of which is the current sigAC
More examples